CDF (Cuber data file) is an universal binary file format, which is created to store any data user wants.
The file consists of the Header, VNT, BNT, TST and Blocks.

VNT (Value names table) — this table(array) stores all the names which are used in all block types for value labeling. Consists of N NULL-terminated strings written one after another (the new one starts just after the last `\0` byte).
BNT (Block names table) — the same table as VNT, but for block types` names storage.
TST (Type specification table) — stores all specifications (types) for the blocks used in the file.
Block — the very meat of the file. Stores the type and an actual bytes array.
At the end, a block functions similar to a C/C++ structure — it can hold some text-labeled values of specified types.
The exact order of these sub-blocks is: Header→VNT→BNT→TST→Data blocks
Header:
Block name	Size(bytes)	Description
sign	4	[`C`,`D`,`F`,`\0`], file signature
version	1	MAJOR version of the CDF format which is used in this file
	1	MINOR one
nnum	4	The length (amount of the names) of the VNT
bnum	4	Same, but for the BNT

MAJOR version marks core changes in the file format, so two different major versions can not be compatible with each other. By default, the engine will refuse loading file if it`s MAJOR version differs from the file`s one.

Block type specification:

Block name		Size(bytes)	Description
nid		4	The index of this type`s name in the BNT
vnum (N)		4	The amount of values in this type
vdata, / vnum times	nid	4	The index of this value`s name in the VNT
	arrb	4	Array info. The length of the array (1 if this is a single value)
	offset	8	The offset from the beginning of the data array where this value starts
	type	1	The type of this value

Block:

Block name	Size(bytes)	Description
tid	4	The index of the type specification in the TST
data	N	Actual data

Supported types:

Name	Index	Size (bytes)
BYTE	1	1
CHAR	2
UINT16	3	2
INT16	4
UINT32	5	4
INT32	6
UINT64	7	8
INT64	8
FLOAT32	9	4